## Slide 1: Chapter 4: Network Layer
Freshman Seminar
2022.02.18
Sumin Sohn

## Slide 2: Contents
4.1 Introduction
4.2 Virtual Circuit and Datagram Networks
4.3 Inside a Router
4.4 The Internet Protocol
4.5 Routing Algorithms
4.6 Routing in the Internet
4.7 Broadcast and Multicast Routing

## Slide 3: 4.1 Introduction

## Slide 4: Forwarding and Routing
Forwarding
  Router transfer a packet from an input link interface to the appropriate output link interface
Routing
  Determining end-to-end paths from source to destination
Forwarding Table
  Router forwards a packet by examining the value of header
Link-layer Switch
  Some router forward the packet based on values in the link-layer frame

## Slide 5: Connection Setup
TCP did a three-way handshake
  Allowing sender and receiver to set up the needed information
Routers along the chosen path
  Setting up the state before connection can begin flow

## Slide 6: Network Services
Guaranteed delivery (with bounded delay)
  Guarantee the packet will arrive(within time limit)
In-order packet delivery
  Guarantee the packet arrives in the order
Guaranteed minimal bandwidth
  Emulates the transmission link of specified bit rate
Guaranteed maximum jitter
  Amount of time between two packets for sender and recipient is same
Security services
  Network layer can also encrypt/decrypt the datagram

## Slide 7: Network Service Models
Network Architecture | Service Model | Bandwidth Guarantee | No-Loss Guarantee | Ordering | Timing | Congestion Indication
Internet | Best effort | None | None | Any order possible | Not maintained | None
ATM | CBR | Guaranteed constant rate | Yes | In order | Maintained | No congestion
ATM | ABR | Guaranteed minimum | None | In order | Not maintained | Congestion indication

## Slide 8: 4.2 Virtual Circuit and Datagram Networks

## Slide 9: The Difference between Virtual Circuit and Datagram Networks
Transport layer provides services to process
  Network layer provides service to host
Virtual circuit network
  Connection-oriented service on network layer
Datagram network
  Connectionless service on network layer

## Slide 10: Virtual-Circuit Networks
Virtual-Circuit consists of
  A path between the source and destination
  VC numbers for each link along the path
  Entries in the forwarding table in each router along the path
When a new VC is established across a router
  Entry is added to the forwarding table
  Replacing the number from link to link
The network’s routers must maintain connection state information

## Slide 11: Identifiable Phases in a Virtual Circuit
VC setup
  The network layer determines the path and VC number between sender and receiver
  Network layer adds an entry in the forwarding table in each router along the path
Data transfer
  Packets begin to flow along the VC
VC teardown
  Terminate the VC
A VC network layer is fully aware of each router along the path

## Slide 12: Datagram Networks
Datagram network stamps the packet with the address of destination end system
Only Address is used to determine corresponding link interface
Routing algorithms update forwarding table

## Slide 13: Longest Prefix Matching Rule
It is possible for a destination address to match more than one entry
It finds the longest matching entry in the table
  E.g., If certain address match the second entry and third entry it matches to the longer entry

## Slide 14: 4.3 Inside a Router

## Slide 15: Router Components
Input ports
  Performs the physical layer function
  Performs the link layer function
  Performs the look up function
Switching fabric
  Interconnects between input ports and output ports
Output ports
Routing processor
  Executes routing protocols
  Maintains connection state information

## Slide 16: Router Plane
It is implemented on the hardware
  Forwarding hardware can be implemented using a router vendor’s own hardware designs
The reason for hardware
  Datagram-processing pipeline is far too fast for software implementation
Router control plane functions are implemented in software

## Slide 17: Input Processing
Line termination function
  Implementing physical layer
Data link processing
  Implementing link layer
Lookup
  Router uses the forwarding table to find appropriate output port
  The reason why hardware implementation is needed
Match desirable action abstraction is not only used on router
  Prevalent in network devices

## Slide 18: Switching via Memory
Switching between input and output ports is done under the control of routing processor
Input port with an arriving packet signaled interrupt
The packet is copied into memory
Processor look up appropriate output port
Processor copies the packet to the output port’s buffers

## Slide 19: Switching via Bus
Input port directly transfers to output ports via bus without intervention of routing processor
Switch label is used to match
  Removed at the output port
Similar to rotary
  Operate in small local area
Switching speed is limited by bus speed

## Slide 20: Switching via an Interconnection Network
Overcoming the bandwidth of single bus
Crossbar switch is an interconnection network
  Connects between input ports and output ports
Capable of forwarding multiple packets in parallel

## Slide 21: Output Processing
Take packets that have been stored in the output port’s memory
Transmit packets over the output link
Must select and de-queue packets
  Perform link-layer and physical layer functions

## Slide 22: The Reason of Queueing
If the processing speed over input port and over output port is not same
  E.g., if switching fabric transfer is much faster than the input/output port speed
Packet loss is occurred if queued memory is no longer available
Output port Queueing
  Packet scheduler chose one packet among queued packets
  Packet scheduling has a crucial role in providing quality-of-service
  Random Early Detection algorithm is used for dropping/marking packets
    Drop – getting rid of packet from the queue
    Mark – mark the header of the certain packet

## Slide 23: Head of Line Blocking
Switching fabric can transfer only one packet to a given output port at a time
The second packet in the third input port memory need to wait
  Waiting for the first packet to be processed
  Not ideal situation since second packet’s destination is different

## Slide 24: 4.4 The Internet Protocol

## Slide 25: Components of Network Layer
IP protocol
  The topic of this section
Routing component
  Determine the path from the source and destination
Facility to report errors and respond to requests for certain network layer information
  ICMP

## Slide 26: IPv4 Datagram Format #1
Version number
  4bits specifying IP protocol version
Header length
  Determine where the data locates
Type of service
  Allow different types of datagrams
  Distinguish real-time from non-real-time
Datagram length
  Total length of datagram
Identifier, Flags, Fragmentation offset
  Used for IP fragmentation – v6 don’t use it

## Slide 27: IPv4 Datagram Format #2
Time to live
  Ensure datagrams do not circulate forever
Protocol
  Used only on a destination
  Binds network layer and transport layer
Header checksum
  Detecting bit errors
IP address
Options
  IP header to be extended deleted on V6
Data

## Slide 28: IP Datagram Fragmentation
Maximum Transmission Unit
  Maximum amount of data that a link-layer can carry
Different MTU
  Fragmentation Occurs
Some fields are used for uniting fragments
Fragmented datagram reassembly in the end system on IPv4

## Slide 29: Example of Fragmentation
Bytes indicates size of data
Original datagram is stamped with ID 777
Offset indicates beginning point
Flag indicates whether the fragment is final fragment or not

## Slide 30: IPv4 Addressing
Interface
  The boundary between the router and any one of links
IP address is associated with an interface
IP address is 32bits long
  E.g.,=>

## Slide 31: Subnet
Subnet
  The network interconnecting interfaces of hosts and router
Subnet mask
  IP address assigned to subnet
  E.g., all hosts within the 223.1.1.0/23
  Share leftmost 24bits of address

## Slide 32: Classless InterDomain Routing
Separate IP address into two parts
  – MSB is
Router only consider leftmost bits
bits are for sorting out hosts within same subnet
Before applying CIDR bits are limited to
  For bits too big , For bits to small
Broadcast address is
  Sent to all hosts within same subnet

## Slide 33: Obtaining a Block of Addresses
Organization can get IP address block from ISP
ISP can get IP address block from ICANN

## Slide 34: Dynamic Host Configuration Protocol
Dynamically allocating IP addresses to host
  Also, allowing a host additional information(address of local DNS server…)
  DHCP server allocates IP address to host within a certain set of addresses
Plug and play protocol
  Automate the procedure of connecting host into a network
Client server protocol
  Newly arriving host obtain network configuration information including IP address

## Slide 35: Four Steps of DHCP #1
DHCP discovery
  Port number 67 UDP packet
  Client make datagram including DHCP discover message
  Source IP address
    Client doesn’t even know his address
  Destination address
  Broadcasts to all nodes attached to the subnet
DHCP offer
  DHCP server receiving discover message responds
  Broadcasts to all nodes
  Including IP address life time

## Slide 36: Four Steps of DHCP #2
DHCP request
  Chose from one or more server offers
    Can exist more than one DHCP server
  Respond by echoing back
DHCP ACK
  Server responds to the DHCP request message

## Slide 37: Network Address Translation
is for private network
Router changes LAN address to WAN address
Router delegates sending packet beyond the interface instead of hosts
NAT translation table is used to distinguish internal hosts
  Different hosts -> Different port numbers

## Slide 38: UPnP
Universal Plug and Play is provided to NAT
A protocol allowing a host to discover and configure nearby NAT
UPnP allows a host to map private IP address and port number to public IP address and port number
  Nodes from the outside can initiate connection with public IP address and port number
Allows external hosts to initiate communication sessions to NATed hosts

## Slide 39: ICMP
Used for error reporting
ICMP messages are carried inside IP datagrams
  Multiplexing and demultiplexing

## Slide 40: IPv6 Datagram Format
The difference from IPv4
  Extended address 32bit -> 128bit
  40byte fixed length header
  Flow labeling and priority
Traffic class
  Similar to TOS in IPv4
Payload length
  Length of data
Hop limit
  Decreases one by each router
Next hdr
  Upper layer protocol

## Slide 41: Deleted IPv4 Fields
Fragmentation/Reassembly
  IPv6 only allow fragmentation/reassembly on end systems
Header checksum
  Does not need check-summing since transport layer and link layer did it
Options
  Options field is extracted to next header pointed from next hdr field
  Fixed 40 bytes header possible

## Slide 42: Transitioning from IPv4 to IPv6
Flag day
  Turning off all internet devices and upgrade
Dual-stack approach
  IPv6/IPv4 node can handle both protocols
  Some fields are dropped if router along the path only handle IPv4 (IPv6 datagram is sent)
Tunneling
  IPv6 datagram is treated as data for IPv4 node

## Slide 43: IPsec’s Transport Mode
Transport layer sends segment to IPsec layer
IPsec encrypts segment append security fields
Encapsulate resulting payload into IP datagram
Services provided by IPsec
  Cryptographic agreement
  Encryption of IP datagram payloads
  Data integrity
  Origin authentication

## Slide 44: 4.5 Routing Algorithms

## Slide 45: Introduction of Routing Algorithms
Default router
  The router attached to host
Destination router
  The router attached to destination
Graph number of nodes collection of edges
  Need to find shortest path from source to destination
  Cost on edge is used for shortest path (cost represents physical length)
  and are neighbor if connected
  Undirected graph
    Cost between and and cost between and are same

## Slide 46: Classification of Routing Algorithms
A global routing algorithm
  Computes least cost path using complete knowledge about network
  Link-state algorithm
A decentralized routing algorithm
  Calculate least cost path with iteration using non-complete knowledge about network
  Distance-vector algorithm
Static/Dynamic routing algorithms
  The speed of path change
Load-sensitive/insensitive algorithms
  Highly depend on link-cost or not

## Slide 47: The Link-State Routing Algorithm
Broadcasting link-state packet is needed
  Each nodes computes path on this information
Dijkstra’s algorithm is used
  – cost of least cost path from source to
  – neighbor of along the path
  - subset of nodes
Adding a least cost edge on each loop
Calculates all possible path on the graph

## Slide 48: Oscillations
First applying LS algorithm determines clock wise sending is least cost
  Adding load into link
After load is added LS algorithm determines counter clock wise is least cost
To prevent oscillations
  Randomize the time algorithm applies

## Slide 49: The Distance Vector Routing Algorithm
Iterative and asynchronous algorithm
Bellman-Ford equation
  on all connected to
  If is updated, notify all routers connected
Each node calculates using neighbor’s distance vector
Next hop router is known using this algorithm

## Slide 50: DV Algorithm : Link-Cost Changes
Node running the DV algorithm detects the link cost change
Update its distance vector and notify its distance vector its neighbors
Neighbors receives update message computes new distance vector and send to its neighbors
gets distance vector from its neighbors
No least cost path changed since ’s link cost is changed

## Slide 51: DV Algorithm : Link Failure
Cost between and is changed to 60
For , , decides best option to go is going through
For , , decides best option to go is going through
Routing loop occurs before z knows cost of path via is larger than 50

## Slide 52: DV Algorithm : Adding Poisoned Reverse
Specific looping scenario can be avoided by using poisoned reverse
Even though renews its path to , will lie to that
route directly to
route directly to
Routing loop doesn’t occur

## Slide 53: Comparison of LS and DV
Message complexity
  LS requires all of the cost on the network
  DV only exchanges message with its neighbor
Speed of convergence
  LS - is always needed
  DV – possibility of routing loop
Robustness
  Malfunction of router can damage all networks

## Slide 54: Hierarchical Routing
Autonomous System of routers
  Scale
    The overhead is too large for handling all nodes in network
  Administrative autonomy
    Able to run by local policy
Intra AS routing protocol
  Routing algorithm running within AS
Gateway router
  Router forwarding to outside of AS
Inter AS routing protocol
  AS communicating each other

## Slide 55: 4.6 Routing in The Internet

## Slide 56: Intra-AS Routing : RIP
Routing Information Protocol
  Based on DV algorithm
  Cost is hop count - each link has 1 cost
RIP response message
  Advertising its routing table to nodes nearby
Each router has routing table
  Including distance vector and forwarding table
RIP is application protocol above UDP

## Slide 57: Intra-AS Routing : OSPF
Open Shortest Path First
  Based on LS
Router broadcasts routing information
Security
  Only authenticated routing information is acknowledged
  Sequence numbers used for preventing replay attack
Support for multicast and unicast routing
Support for hierarchy
  Can be configured into areas
  Backbone area route traffic between the other areas
  Backbone area interconnect between the areas

## Slide 58: Inter-AS Routing : BGP
BGP provides services to AS
  Obtain reachability information from neighbor ASs
  Propagate reachability information to all neighbor ASs
  Determine path
BGP basics
  eBGP session
    TCP session between ASs
  iBGP session
    TCP session in the same AS
  BGP peers
    Two routers at the end of connection

## Slide 59: Path Attributes and BGP Routes
BGP advertises its subnets by using prefix
Router also includes a number of BGP attributes when advertising
  AS-PATH
    ASs through which advertisement has passed
    Used to configure forwarding tables
  NEXT-HOP
    Router interface that begins AS-PATH
BGP route selection
  Routes with the highest preference are selected
  Routes with the shortest AS-PATH are selected
  Route with the closest NEXT-HOP router is selected

## Slide 60: 4.7 Broadcast and Multicast Routing

## Slide 61: Broadcast Routing Algorithm
Broadcast Routing
  Send packet to all other nodes in the network
-way-unicast
  Copy packets and send it all
  Inefficiency
  Address is needed
  Unwise to rely on unicast routing to broadcast on LS algorithm
Uncontrolled Flooding
  Node send packet all of its neighbors
  Broadcast storm can occur

## Slide 62: Broadcast Routing Algorithm : Controlled Flooding
Sequence number controlled flooding
  Save already received broadcast packet with a sequence number
Reverse path forwarding
  Only receive the packet if the path that packet is sent is shortest path from the source
  If above condition is fulfilled, broadcast
  E.g., B ignore packet from C since packet through C is not the shortest path from A

## Slide 63: Broadcast Routing Algorithm : Spanning Tree Broadcast
Spanning tree
  A tree that contains every node in graph
  No cycle
Source node send the broadcast packet along the spanning tree
Center-based approach
  E.g., E is center node
  Spanning tree is constructed starting from E

## Slide 64: Multicast
Sending packet to certain group
  E.g., Streaming
Use address indirection
Different Host with Different address is associated with multicast group
IGMP is used for taking care of group
  Internet Group Management Protocol

## Slide 65: IGMP
IGMP operates between a host and directly attached router
All hosts in LAN receive
Host wanting a group respond with
Host first joining a group can send
If no response from
  IGMP consider no hosts want to participate in the group

## Slide 66: Multicast Routing Algorithm
Group shared tree multicast
  Router within group make spanning tree
  Can include the router not associated with multicast
Source based tree multicast
  Use PRF algorithm to establish tree
  Pruning
    Delete non-multicast node from tree

## Slide 67: Conclusion
Change virtual circuit to datagram to make router’s job easier
Learn how router really works by examining inside of router
IPv4 and IPv6
Routing algorithm is needed to determine the best path
Learn how broadcasting and multicasting works