## Slide 1: Chapter 5: The Link Layer – Links, Access, Networks, and LANs
Freshman Seminar
2022.03.02
Sumin Sohn

## Slide 2: Contents
5.1 Introduction to the link layer
5.2 Error-detection and –correction techniques
5.3 Multiple access links and protocols
5.4 Switched local area networks

## Slide 3: 5.1 Introduction to the link layer

## Slide 4: Terminology
Node
  Any device that runs in link-layer protocol
  E.g., host, router, switch, WiFi access point
Link
  Communication channel that connect adjacent nodes
Link-layer frame
  Over a given link, transmitting node encapsulate datagram in link-layer frame
  Consist of data field(datagram) and headers
    Structure is specified by link-layer protocol

## Slide 5: Services of Link Layer #1
Basic service: move a datagram from one node to adjacent node over link
Possible services by link-layer protocol
  Framing
    Encapsulate each network-layer datagram within a link-layer frame
  Link access
    Medium Access Control(MAC) protocol specifies rules by which frame is transmitted onto link
    When multiple nodes share a single broadcast link
      MAC protocol serve to coordinate frame transmission of many nodes
  Reliable delivery
    Guarantee to move each network-layer datagram across the link without error
    Often used for links that are prone to high error rates with goal of correcting error locally
      E.g., wireless link

## Slide 6: Services of Link Layer #2
(Cont.) Possible services by link-layer protocol
  Error detection and correction
    Bit errors are introduced by signal attenuation and electro-magnetic noise
    Error detection is usually more sophisticated and implemented in hardware
    For error correction,
      Receiver detect bit error in frame
      And also, determine where in frame errors have occurred

## Slide 7: Link-Layer Implementation in Hardware
For most part, link layer is implemented in network adapter
  Known as Network Interface Card(NIC)
  Attached to host’s bus
Heart of network adapter is link-layer controller
  Implements of many link-layer services
  Framing, link access, error detection, etc.
Much of controller’s functionality is implemented in hardware
Notes: End system의 link layer에 포커싱

## Slide 8: Link-Layer Implementation in Software
Part of link layer is implemented in software
  Run on host’s CPU
Implement high-level functionality
  Assemble link-layer addressing information
  Activate controller hardware
E.g., on receiving side,
  Respond to controller interrupt
  Handle error condition and pass datagram up to network layer
Thus, link layer is combination of HW and SW

## Slide 9: 5.2 Error-detection and –correction techniques

## Slide 10: Error Detection and Correction Scenario
Sender
  Data is protected against bit errors with Error-Detection and Correction bits(EDC)
  Data include
    Datagram
    Link-layered packet
Receiver
  Determine whether or not received D’ is same as original D
  Sometimes, there still may undetected bit errors
    Should be small possibility of such errors
Notes: Undetected bit error가 작을 수 있도록 하는게 필요
약간의 trade off가 생기게 됨
정교할수록 undetected bit error는 줄겠지만,
그만큼의 오버헤드도 고려해야하니까

## Slide 11: Three Techniques for Detecting Errors
Parity check
  Basic idea behind error detection and correction
Checksumming method
  Typically used in transport layer
Cyclic redundancy check
  Typically used in link layer

## Slide 12: Single Parity Bit Checks
Even parity scheme
  Sender
    Include one additional bit
    Choose value that total number of 1s in bits is even
  Receiver
    Count number of 1s in received bits
What if even number of bit errors occur?
  Would be undetected error
  Problematic if errors are clustered in burst
    More robust scheme is needed
Even parity scheme
Notes: Single bit check는 error가 클러스터되어서 터지는 경우 문제가 될 수 있음

## Slide 13: Two-Dimensional Parity Scheme
Scheme
  bits in are divided into rows andcolumns
  Parity value is computed for each row and column
  Resulting parity bits are error-detection bits
In this scheme, receiver can
  Detect single bit error
  Identify corrupted bit and correct
    Using column and row indices
  However, it can detect but not correct combination of two error

## Slide 14: Forward Error Correction(FEC)
Ability of receiver to both detect and correct errors
Values of FEC
  Used with link layer ARQ
  Decrease number of sender retransmission required
  Allow for immediate correction of errors at receiver
    No delay for sender to receive NAK and for retransmitted packet to propagate to receiver

## Slide 15: Checksumming Methods
Approach: simply sum -bit integers and use sum as error-detection bits
E.g., Internet checksum
  Sender
    Bytes of data are treated as 16-bit integers and summed
    1s complement of sum
  Receiver
    Check checksum by taking 1s complement for sum of received data including checksum
    If any of bits are 0, error is indicated
Relatively little packet overhead but weak protection compared to cyclic redundancy check
  Then why this method is used in transport layer?

## Slide 16: Different Error Handling in Each Layers
Transport layer is implemented in software
  Important to have simple and fast error-detection scheme
  Such as, checksumming
Link layer is implemented in dedicated hardware in adapter
  Rapidly perform more complex operations
Notes: Link layer는 전용 하드웨어인 adapter에 구현되어있음

## Slide 17: Cyclic Redundancy Check(CRC) Codes
CRC codes known as polynomial codes
  View bit string as polynomial whose coefficients are 0 and 1
Operation
  Sender and receiver must agree on bit pattern, known as generator
    Most significant bit of should be 1
  For given data , sender choose additional -bits and attack to
  Process of error checking
    Receiver divides bits by
    If remainder 0, error has occurred

## Slide 18: CRC Calculations
Done in modulo-2 arithmetic
  Without carries in addition or borrows in subtraction
  Equivalent to bitwise XOR()
  Multiplication by left shifts a bit pattern by places
  Add(XOR) additional
Compute : remainder of
    For dividing by , remainder is
Example of Calculating R

## Slide 19: Error Detection of CRC
CRC standard can detect burst errors of fewer than bits
Burst of errors greater than bits is detected with possibility

## Slide 20: 5.3 Multiple access links and protocols

## Slide 21: Two Types of Network Links
Point-to-point link
  Consist of single sender and single receiver at each end of the link
Broadcast link
  Have multiple sending and receiving nodes
    Connected to same, single, shared broadcast channel
  Collide occurs if over two node use same link at the same time
  E.g., ethernet and wireless LANs

## Slide 22: Multiple Access Protocol
Nodes regulate their transmission into shared broadcast channel
  By multiple access protocol
Because all nodes are capable of transmitting frames,
  More than two nodes can transmit frames at same time
  All of nodes receive multiple frames at same time
  In a sense, signals of colliding frames become tangled together
    All frames involved in collision are lost
    Broadcast channel is wasted during collision interval
Notes: Shared channel에 대한 node의 접근을 어떻게 조정. 편성할 것인가
In a sense, 어떤 의미에서는

## Slide 23: Desirable Characteristics of Multiple Access Protocol
When only one node has data to send
  Node has throughput of bps
When M nodes have data to send
  Each of nodes has average throughput of bps
Protocol is decentralized
  No master node that represent a single point of failure for network
Protocol is simple
  Inexpensive to implement

## Slide 24: Three Categories of Multiple Access Protocol
Channel partitioning protocols
Random access protocols
Taking-turns protocols
Notes: Channel Partitioning: 채널을 여러 작은 조각들로 나누어서 분배한다.(time slots, frequency, code) 즉 각각 노드마다 배타적인 사용을 하기 위해서 할당한다고 볼 수 있겠다.
Random access: 이건 그냥 보내고 싶을 때 보내는 방법이라고 할 수 있다. Collision을 수용하는 방식이라고 생각하면 된다. 이는 채널에 속해 있는 단말의 수가 적을 때 택할 수 있는 방법이다. 만약 Collision이 발생하면, 그냥 다시 보낸다!
Taking turns: 돌아가면서 보낼 수 있는 방법을 말한다. 다 똑같이 보낼 시간을 주는 것이 아닌, 보내려는 양이 더 많은 노드의 경우에는 더 오랫동안 보낼 수 있다.
https://team00csduck.tistory.com/157

## Slide 25: Channel Partitioning Protocols: Time-Division Multiplexing(TDM)
Used to partition broadcast channel’s bandwidth among all sharing nodes
TDM share broadcast in time
  Divide into time frame
  Divide each time frame into slots
    Single packet can be transmitted in time slot
  Each slot is assigned to one of nodes
  Whenever a node has packet to send,
    Transmit packet’s bits during time slot

## Slide 26: Advantages and Drawbacks of TDM
Advantages
  Eliminate collision and is perfectly fair
    Each node gets a dedicated transmission rate of bps during each frame time
Drawbacks
  Node is limited to average rate of bps
    Even when it is the only node with packets to send
  Node must always wait for its turn in transmission sequence

## Slide 27: Channel Partitioning Protocols: Frequency-Division Multiplexing(FDM)
FDM create smaller channels of bps out of single, larger bps channel
  Divide bps channel into different frequencies
    Each with a bandwidth of bps
  Assign each frequency to one of nodes
Advantages
  Avoid collision
  Divide bandwidth fairly among nodes
Drawbacks
  Node is limited to bandwidth of
    Even when it is only node with packets to send
Notes: https://talkingaboutme.tistory.com/entry/Signal-Frequency-Division-Multiplexing

## Slide 28: Channel Partitioning Protocols: Code Division Multiple Access(CDMA)
Approach
  Assign different code to each node
  Each node use its unique code to encode data bits
  Different nodes can transmit simultaneously
  Receivers correctly receive sender’s encoded data bits
    Assume receiver knows sender’s code
Particularly use for cellular telephony
  Cellular
    Mobile telephone system
Notes: 따라서 Channel Partitioning 방법은 네트워크에 있는 기기의 숫자가 정해져 있고, 각각 처리량이 많을 때, 유용한 프로토콜이라고 할 수 있다.

## Slide 29: Random Access Protocols
Approach
  Transmitting node always transmit at full rate of channel
  When there is collision, each node involved in collision repeatedly retransmit its frame
    Until its frame gets through without collision
  However, it waits a random delay before retransmitting frame
    Random delays are independently chosen
    So, be able to sneak it frame into channel without collision
Protocols
  Slotted Aloha and Aloha
  Carrier Sense Multiple Access(CSMA)
  Carrier Sense Multiple Access with Collision Detection(CSMA/CD)
Notes: Get through 통과하다 빠져나가다
Retransmit이 바로 되는 게 아니고, random delay를 거쳐서 한다
- 이게 결국에는 노드마다 다른 delay를 가지고 보내지게 될 거니까
- 서로 시간 차를 두고 보내지게 되는 것

## Slide 30: Assumption of Slotted Aloha
All frames consist of exactly bits
Time is divided into slots of size seconds
  That is, a slot equals the time to transmit one frame
Nodes start to transmit frames only at the beginnings of slots
Nodes are synchronized so that each node knows when the slots begin
If two or more frames collide in a slot, all nodes detect collision event before the slot ends

## Slide 31: Operation of Slotted Aloha
When node has a fresh frame to send,
  It waits until the beginning of the next slot
  And transmits the entire frame in the slot
If no collision occurs,
  Node has successfully transmitted its frame and thus no retransmission
  Node can prepare a new frame for transmission, if it has one
If collision occurs,
  Node detects the collision before the end of the slot.
  Node retransmits its frame in each subsequent slot with probability
    Until frame is transmitted without collision

## Slide 32: Advantages of Slotted Aloha
Allow a node to transmit continuously at the full rate
  When the node is the only active node
Highly decentralized
  Because each node detects collisions and independently decides when to retransmit

## Slide 33: Two Possible Efficiency Concerns
Collision slot
  When there are multiple active nodes
  Collision occurs, and therefore wasted
Empty slot
  Because all active nodes refrain from probabilistic transmitting
Successful slot
  Slot in which exactly one node transmit
So, the efficiency
  For N active nodes,
    : probability of transmission
  Maximum efficiency is given by = 0.37
Notes: Refrain 그만두다
P의 확률로 보낸다고 하면, 1-p의 확률로 안 보낼 수도 있는 것
성공하기 위해서는 1개는 보내야 하고, 나머지는 모두 안 보내야 하니까

## Slide 34: Protocol Before Slotted Aloha: Aloha
Unslotted, fully decentralized protocol
Nodes don’t know about starting time
Procedure
  Node immediately transmit frame into broadcast channel
  If collision occurs,
    Node immediately retransmit frame with probability
  Otherwise,
    Node waits for a frame transmission time
Maximum efficiency
  Exactly half of slotted Aloha

## Slide 35: Rules for CSMA
Carrier sensing
  Node listen to the channel before transmitting
  If frame is currently being transmitted into channel
    Node waits until it detects no transmission
Collision detection
  Transmitting node listen to channel while it is transmitting
  If it detects that another node is transmitting an interfering frame
    Stop transmitting and wait random amount of time

## Slide 36: Carrier Sense Multiple Access(CSMA)
Why collision occur even though all nodes perform carrier sensing in rules?
  Due to end-to-end propagation delay
End-to-end propagation delay
  Time it takes for signal to propagate from one of nodes to another
  Situation
    At time , node B sense channel is idle
    At time , node D sense channel is idle
      Bits transmitted by B have yet reached to D
    Short time later, B’s transmission begins to interfere with D’s transmission
  Shorter delay is better
Both B and D transmit in spite of collision

## Slide 37: Carrier Sense Multiple Access with Collision Detection(CSMA/CD)
Nodes abort transmission after detecting collision
  Not transmitting a useless, damaged frame in its entirety
Operation from perspective of adapter
  When adapter obtains datagram,
    Prepares a link-layer frame, and puts the frame adapter buffer
  If adapter senses that the channel is idle, transmit the frame
    Otherwise, wait until it senses no signal energy and then transmit
  While transmitting,
    Adapter monitors signal from other adapters using the broadcast channel

## Slide 38: Carrier Sense Multiple Access with Collision Detection(CSMA/CD)
(Cont.) Operation from perspective of adapter
  If adapter transmits entire frame without detecting signal from other adapters,
    Adapter is finished with the frame
    Otherwise, stops transmitting its frame
  After aborting,
    Adapter waits a random amount of time and then returns to step 2
Need for random amount of time
  If two nodes transmit at the same time, continue colliding forever
Then what is good interval to choose random backoff time?
Notes: Interval 설정이 적절하게 되어야 하는게,
- 너무 작으면 colliding이 자주 발생
- 너무 크면 node가 오래 기다려야 하니까

## Slide 39: Binary Exponential Backoff
When transmitting a frame that has already experienced collisions
  Node choose value of at random from
  E.g., for ethernet, amount of waiting time is bit times
Size of sets grows exponentially with number of collisions
Each time node prepares a new frame for transmission
  Run CSMA/CD algorithm
  Not consider any collisions that may have occurred in recent past
    Can sneak in successful transmission, while other nodes are in exponential backoff state

## Slide 40: Efficiency of CSMA/CD
Efficiency:
  : maximum time it takes signal to propagate between two adapters
  : time to transmit a maximum size frame
Interpretation of formula
  If approaches 0, efficiency approaches 1
    If propagation delay is zero, colliding node abort immediately
  If becomes large, efficiency approaches 1
    When a frame grab channel, hold onto channel for a very long time
Notes: Prop: 두 adapter 사이에 propagate하는 데 걸리는 최대 시간
Trans: maximum 크기의 frame 보는데 걸리는 시간

## Slide 41: CSMA/CA

## Slide 42: CSMA/CA vs CSMA/CD
Instead of using collision detection, it uses collision-avoidance techniques
  Once, a station begins to transmit a frame it transmit the frame entirely
  No turning back
Uses link-layer acknowledgment/retransmission(ARQ) scheme
Used in wireless environment with relatively high bit error rate

## Slide 43: Why Not Implement Collision Detection?
Ability to detect collision requires ability to send and receive at the same time
  More costly to implement
Even if the adapter could transmit and listen at the same time, adapter would still not be able to detect all collisions due to hidden terminal problem

## Slide 44: Hidden Terminal Problem
Due to fading each host are hidden from each other although neither is hidden from AP
Host H1 and H2 may send frames at same time to AP causing collision
  Cannot detect each other, therefore hidden

## Slide 45: CSMA/CA Procedure
If channel is idle, wait for short period of time known as Distributed Inter-frame Space(DIFS)
If channel is still idle, transmit frame and wait for ACK
Otherwise wait for time using binary exponential backoff
If channel is idle, count down the value
Otherwise, counter remains frozen
When counter reaches zero, the station transmits frame and wait for ACK
If ACK has not been received retransmit by going to step 3

## Slide 46: Clear to Send(CTS) & Request to Send(RTS)
Mitigated with short control frames: CTS, RTS
Request to send(RTS)
  When sender wants to send data frame, it first broadcast RTS frame
Clear to send(CTS)
  When AP receives RTS frame, it responds by broadcasting CTS frame
  Two purposes of CTS frame
    Give sender explicit permission to send
    Instructs other stations to not send for certain amount of time reserved in CTS frame
  Since two hosts are in range of AP, hidden terminal problem is mitigated

## Slide 47: Taking-Turns Protocols
Aloha and CSMA don’t satisfy property that
  When M nodes are active, then each active node has a throughput of nearly R/M bps
  This is, the motivation for taking-turns protocols
Taking-turns protocols
  Polling protocol
  Token-passing protocol

## Slide 48: Polling Protocol
Requirement: one of nodes to be designated as master node
Procedure
  Master node poll each of the nodes in round-robin fashion
    Continue in cyclic manner
Advantages
  Eliminate collision and empty slot
Drawbacks
  Introduce polling delay
    Delay : amount of time required to notify a node that it can transmit
    So, node can transmit at a rate less than R bps
  If master node fails, entire channel becomes inoperative
Notes: Polling: 정기적으로 정보를 수집하는 걸 말함
- 나한테 데이터 보낼래? Call 던져서 보내게하는 걸 말함
Round robin fashio으로 동작을 한다는게,
Master가 1번 노드한테 얼마까지 보낼 수 있다고 알리면, 노드 1이 frame들을 보냄
그 후에, 노드 2한테 얼마까지 보낼 수 있다고 하면, 또 노드 2가 frame을 보냄

## Slide 49: Token-Passing Protocol
Requirement: token
Procedure
  Token is exchanged among nodes in some fixed order
  When a node receives a token
    If node has frames to send,
      Holds onto token
      Send up to maximum number of frames and then forward token to next node
    Otherwise, immediately forwards token
Problems
  Failure of one node can crash entire channel
  If a node accidentally neglect to release token, recovery must be invoked
Notes: 여기서 fixed order라는게, 1은 반드시 2에게 token을 보내야하고, 2는 3에게 보내야하고, 이렇게 정해진 순서를 말함

## Slide 50: DOCSIS: The Link-Layer Protocol for Cable Internet Access #1
Cable access network
  Connect residential cable modems to Cable Modem Termination System(CMTS)
Use FDM
  To divide downstream/upstream network segments into multiple frequency channels
Each upstream channel is divided into intervals of time(TDM-like)
  Since collision can occur in upstream
  CTMS explicitly grants permission to individual modems to transmit during slots
Notes: FDM이용해서 downstream/upstream segment 나눔
downstream: 6MHZ / upstream 6.4MHz
Downstream에서는 multiple access problem이 발생하지 않음
Upstream에서는 여러 개의 modem이 같은 upstream channel을 공유하기 때문에 collision이 발생할 수 있음
Permission을 주는 방식은 MAP message를 downstream에 보냄

## Slide 51: DOCSIS: The Link-Layer Protocol for Cable Internet Access #2
Mini-slot-request frames are transmitted in random access manner
  During special set of interval mini-slots
  By this request, CMTS can know which cable modems have data to send
Cable Modem assumes
  Collision,
    If no message received in downstream channel
    Use binary exponential backoff to defer retransmission of request
CMTS allocate time slot to each modems centrally
Notes: FDM이용해서 downstream/upstream segment 나눔
downstream: 6MHZ / upstream 6.4MHz
Downstream에서는 multiple access problem이 발생하지 않음
Upstream에서는 여러 개의 modem이 같은 upstream channel을 공유하기 때문에 collision이 발생할 수 있음
Permission을 주는 방식은 MAP message를 downstream에 보냄
Defer = 미루다

## Slide 52: 5.4 Switched local area networks

## Slide 53: MAC Address and its Feature
Hosts and routers have link-layer address in network interfaces
Link-layer switches do not have link-layer addresses
  Because job of link-layer switch is to carry datagrams between hosts and routers
Link-layer address is called to MAC address
  6 bytes long and expressed in hexadecimal notation
  Designed to be permanent
No two adapters have same address
  IEEE allocate chunk of addresses by fixing first 24 bits
  And let company create unique combinations of last 24 bits for each adapter
MAC address has a flat structure and doesn’t change where adapter goes
Notes: Flat structure는 hierarchy를 가지는 것과 대비대는 특성임

## Slide 54: The Reason of MAC Address
LANs are designed for arbitrary network protocols
  With MAC address, can support other network protocols
If network address is used instead of MAC address,
  Must be changed whenever adapter is moved
Separate address needed for separate layered architecture

## Slide 55: Sending/Receiving a Frame Using MAC Address
When adapter want to send a frame
  Adapter construct link-layer frame containing destination’s MAC address
    For sending to all other adapters, set FF-FF-FF-FF-FF-FF
  Send frame into LAN
  Switch broadcast incoming frame onto all of its interfaces
When adapter receive a frame
  Check whether destination MAC address in frame matches its own MAC address
  If match,
    Adapter extract datagram and pass it up the protocol stack
  Otherwise,
    Discard frame without passing up

## Slide 56: Address Resolution Protocol(ARP)
To send datagram,
  Source must give its adapter IP datagram and MAC address for destination
How sender determine MAC address?
  Use ARP
  Sender provides its ARP module IP address, and ARP module return MAC address
ARP resolve IP addresses only for hosts and router interfaces
  On the same subnet
Notes: MAC address 얻는 방식
- Sending host가 ARP module에 destination IP 얹어서 물어보면, MAC 주소 반환

## Slide 57: How ARP Works inside of Subnet?
Host and router have ARP table in memory
  Contain mapping of IP addresses to MAC addresses
  Also, contain time-to-live(TTL)
    Indicate when each mapping will be deleted
  Not necessarily contain entry for all hosts and routers on subnet
What if ARP table doesn’t have entry for destination?
  Use ARP protocol to resolve address
  Sender construct ARP query packet
    Query all other hosts and routers on subnet to determine MAC address
    Use broadcast address
ARP table
Subnet
Notes: 설명 다하고, 어떻게 MAC 주소 얻는지 예시 설명
1. ARP 쿼리가 서브넷에 있는 모든 어댑터에게 보내짐
2. 각 어댑터는 ARP 패킷을 ARP 모듈로 올려 보낸 다음, destination IP 주소와 매칭되는지 확인
3. 매칭되면 MAC 주소 알려주고,
4. ARP table 업데이트하고
5. 이제 그러면 sender가 원하는 대로 보낼 수 있게 됨

## Slide 58: Features of ARP
Query ARP message is sent within broadcast frame
  Whereas response ARP message is sent within standard frame
ARP is plug-and-play protocol
  ARP table gets built automatically
ARP straddles boundary between link and network layers
Notes: 사이라고 생각할 수 있는 이유가
Link layer frame으로 감싸니까, link layer 위에 있다고 볼 수도 있지만,
또 ARP packet 자체에 link layer address 같은 필드 포함하니까 어떻게 보면 link layer protocol이라고 할 수도 있음

## Slide 59: Sending a Datagram off the Subnet #1
Host on subnet 1 send a datagram to host on subnet 2
  From 111.111.111.111 to 222.222.222.222
Procedure
  Datagram must first be sent to router interface 111.111.111.110
    IP address of first-hop router
    So, appropriate MAC address is E6-E9-00-17-BB-4B
      Obtained by ARP
  Router adapter on subnet 1 passes the frame to network layer
  And forward into correct interface by forwarding table
Notes: 222.222.222.222의 MAC 주소를 바로 사용하지 않는 것에 주의
- 왜냐? Frame의 destination 주소가 subnet 1에 있는 어떤 어댑터의 주소와도 맞지 않기 때문에 datagram은 죽게 됨

## Slide 60: Sending a Datagram off the Subnet #2
(Cont.) Procedure
  On forwarded interface
    Send datagram into adapter
    Encapsulate datagram into new frame
      At this time, use MAC address of ultimate destination
      Obtained by ARP
    Send frame into subnet2
Notes: 222.222.222.222의 MAC 주소를 바로 사용하지 않는 것에 주의
- 왜냐? Frame의 destination 주소가 subnet 1에 있는 어떤 어댑터의 주소와도 맞지 않기 때문에 datagram은 죽게 됨

## Slide 61: Comparison of Layers #Transport Layer
Operates on end-to-end hosts
In charge of sending network packets into appropriate applications
  Via socket
In charge of congestion control
  For the circumstances packet loss/error occurs
Don’t have any idea of how layer below works
Provide logical connection to applications from other hosts
  Making Developer’s job much easier

## Slide 62: Comparison of Layers #Network Layer
In charge of setting paths using routing algorithm
In charge of interconnecting over the world
For IP protocol, IP address is specified
Layer for large range of sending

## Slide 63: Comparison of Layers #Link Layer
In charge of sending between links and links
Solve broadcast channel problem if solved by several hosts at the same time
Represent device’s address by MAC address
Several protocol is provided to avoid signal interference

## Slide 64: Conclusion
Understand link layer services and implementation
Three error detection techniques
  Parity check
  Checksumming
  CRC code
Multiple Access Problem
  Several protocols
MAC Address