## Slide 1: QnA
Freshman Seminar
2022.03.02.
Sumin Sohn

## Slide 2: The Meaning of Maximum Jitter
Network jitter
  The delay between two successive packets
Guaranteed Maximum jitter
  The delay between two successive packets is no larger than maximum delay

## Slide 3: ATM CBR
Asynchronous Transfer Mode
  Telecommunications standard for digital transmission
  ATM uses connection-oriented model
    Establish a virtual circuit
  It maps physical, link, network layers
  All ATM packets are the same small size
Constant Bit Rate
  One of the services ATM provides
  Maximum transmission rate is specified as constant
  Making a packets flowing pipe

## Slide 4: ATM ABR
Congestion control is provided
Bit rate is changed according to the information in the RM cell
RM cell
  Congestion information included

## Slide 5: Private Addresses
IP Address Range | Number of Addresses
10.0.0.0 – 10.255.255.255 | 16777216
172.16.0.0 – 172.31.255.255 | 1048576
192.168.0.0 – 192.168.255.255 | 65536

## Slide 6: Classful Addressing
At first, 5 Classes are defined
  Lack of IPv4 addresses
  Class C has 8 bit address for assigned address
Classless Addressing
  Subnet has variable range
  Deficiency of address is solved
CLASS | Leading Bits | Starting Address | Ending Address
Class A | 0 | 0.0.0.0 | 127.255.255.255
Class B | 10 | 128.0.0.0 | 191.255.255.255
Class C | 110 | 192.0.0.0 | 223.255.255.255
Class D (Multicast) | 1110 | 224.0.0.0 | 239.255.255.255
Class E (Reserved) | 1111 | 240.0.0.0 | 255.255.255.255